## Slide 1: Reducing Refresh Power in Mobile Devices with Morphable ECC
Chiachen Chou, Georgia Tech
Prashant Nair, Georgia Tech
Moinuddin K. Qureshi, Georgia Tech
DSN-45
06/24/2015
Rio de Janeiro, Brazil
Computer Architecture and Emerging Technologies Lab, Georgia Tech

## Slide 2: GROWING DRAM size in smartphones
Samsung Galaxy S6 (2015)
3GB DRAM
Samsung Galaxy S2 (2011)
1GB DRAM
courtesy: Samsung
Smartphone usability: battery life
30% energy goes to memory system in idle mode
DRAM Refresh accounts for significant energy consumption in idle mode

## Slide 3: Lower Refresh Rate for Energy
Current standard refresh rate: 64ms
DRAM
CPU
64ms
Energy
1X
1s
0.5X
Refresh Rate
Use ECC to protect DRAM from refresh errors
Bit Error Rate
10-9
10-4

## Slide 4: Ecc-6 incurs long latency for read
Decoder latency is on the critical path
DRAM
CPU
Request
ECC
Decoder
Data
ECC-6: 30 cycles
We want energy reduction in idle mode, and maintain performance in active mode

## Slide 5: Agenda
Introduction
Background
  DRAM 101
  Refresh and Errors
  Error Correction Codes (ECC)
Morphable ECC
Results
Summary

## Slide 6: DRAM 101
Dynamic Random Access Memory (DRAM)
DRAM stores data as charge on capacitor
Leakage
DRAM Chip
1
DRAM is a volatile memory  charges leak quickly

## Slide 7: DRAM Refresh
DRAM maintains data integrity by Refresh operations
DRAM Chip
Refresh
Refresh
Refresh
Refresh
JEDEC: 64ms
1s
Lowering refresh rate reduces power
Chart: Refresh Power
| 64ms | 1s
Refresh | 1 | 0.0625
Chart: Idle Power
| 64ms | 1s
Background | 0.5 | 0.5
Refresh | 0.5 | 0.03125
16X
50%

## Slide 8: DRAM Refresh Rate and Errors
DRAM maintains data integrity by Refresh operations
Lowering refresh rate increases bit error rate
Chart: Refresh Rate (second)
| 0.064 | 0.1 | 0.2 | 0.4 | 0.6 | 0.8 | 1.0 | 3.0 | 7.0 | 10.0 | 100.0
Bit Error Rate | 1e-09 | 2e-09 | 8e-09 | 4e-07 | 1e-06 | 9e-06 | 4e-05 | 0.0008 | 0.009 | 0.08 | 0.9
64ms: 10-9
1s: 10-4.5

## Slide 9: Error correction code (ECC)
ECC: tolerate refresh errors
Q: how many errors should the system tolerate?
ECC-1
ECC-6
64B cache line
Errors
1 Error
6 Errors
ECC Strength
Capability

## Slide 10: Error correction code (ECC)
ECC: tolerate refresh errors
Q: how many errors should the system tolerate?
 What should be the strength of the ECC?
ECC Strength | Line Failure | System Failure
ECC-1 | 1.8 X 10-2 | 1.0
ECC-2 | 9.8 X 10-7 | 1.0
ECC-4 | 1.6 X 10-11 | 2.7 X 10-4
ECC-5 | 4.9 X 10-14 | 8.1 X 10-7
ECC-6 | 1.2 X 10-16 | 1.8 X 10-9
Refresh rate of 1s needs ECC-6 for errors
✔
Good
✔

## Slide 11: Drawbacks of ECC-6
Single Core, 1MB Cache, 1GB DRAM
ECC-6 incurs huge performance degradation
Chart: Memory Activity (MPKI)
| Low | Med | High | ALL
ECC-1 | 0.99875 | 0.98936 | 0.98532 | 0.99
ECC-6 | 0.98115 | 0.89838 | 0.84919 | 0.9

## Slide 12: What is the ideal case?
 | Goal | Strong ECC | Weak ECC
Active Mode | Performance (Refresh Power Negligible) | Bad | Good
Idle Mode | Energy (Performance Not Critical) | Good | Bad
✔
✔
✘
✘
Ideally, we want ECC-1 in active mode, and ECC-6 in idle mode
?
?

## Slide 13: Agenda
Introduction
Background
Morphable ECC (MECC)
  Overview
  Design
  ECC Support and Storage
Results
Summary

## Slide 14: MECC: Overview
MECC uses two ECCs based on modes
Time
REFRESH | Normal | Slow | Normal
ECC | Weak | Strong | Weak
Active
Active
Idle
Sleep
Wake up
ECC-Upgrade
ECC-Downgrade
ECC-Upgrade
ECC-Downgrade

## Slide 15: MECC: Design
Memory controller uses ECC-mode bits to decode with different ECCs
DRAM Chips
RD Queue
WR Queue
ECC
Encoder
Address
Data+ECC
Data+ECC
ECC-1
Encoder
ECC-6
Encoder
Memory Controller
To Processor
Data
?
M
0
ECC-Mode
ECC-Mode
Data + ECC
ECC
Decoder

## Slide 16: MECC: ECC storage
64B Data Block
8B ECC
SECDEC
SECDEC
SECDEC
SECDEC
Byte 0-7
Byte 8-15
Byte 48-55
Byte 56-63
Conventional
MECC ECC-1
MECC ECC-6
0000
1111
ECC-Mode
ECC-1 for 64B Data
ECC-6 for 64B Data
60 bits
11 bits
Unused
MECC uses existing space to store 2 ECCs
11 bits
60 bits
+
= 60 bits

## Slide 17: Agenda
Introduction
Background
Morphable ECC
Results
Summary

## Slide 18: methodology
Core Chips:
1 cores 1.6 GHz
2-wide In-Order
1MB cache
Off-chip DRAM
CPU
 | LPDDR2
Capacity | 1GB
Bus | DDR 200MGHz
Organization | 1 channels, 4 banks
Baseline: No Error Correction Code
SPEC2006 (exclude mcf): low, medium, high MPKI workloads
USIMM for DRAM model and power

## Slide 19: Power And energy consumption
Parameters | Values | Description
VDD | 1.7 V | Operating Voltage
IDD0 | 95 mA | 1 bank active precharge current
IDD2P | 0.6 mA | Precharge power-down standby current
IDD3P | 3 mA | Active power-down standby current
IDD4 | 135 mA | Burst read/write: 1 bank active
IDD5 | 100 mA | Auto refresh
IDD8 | 1.3 mA | Self refresh
Power in Idle Mode = (Prefresh original * Toriginal / TMECC ) + Pother
courtesy: Micron LPDDR2 Specs

## Slide 20: Performance in active mode
Chart: Performance
| povray | tonto | wrf | gamess | hmmer | sjeng | h264ref | namd | gobmk | gromacs | perl | astar | bzip2 | dealII | soplex | cactus | calculix | gcc | zeusmp | omnetpp | sphinx | milc | xalanc | leslie | libq | Gems | lbm | bwaves | ALL
ECC-6 | 1 | 0.995 | 0.995 | 0.98 | 0.975 | 0.975 | 0.975 | 0.955 | 0 | 0.95 | 0.93 | 0.925 | 0.93 | 0.91 | 0.899 | 0.885 | 0.89 | 0.87 | 0.83 | 0.87 | 0 | 0.81 | 0.825 | 0.935 | 0.91 | 0.835 | 0.78 | 0.87 | 0.88 | 0.81 | 0 | 0.9
MECC | 1 | 1 | 1 | 1 | 0.995 | 0.987 | 0.995 | 0.99 | 0 | 0.995 | 0.995 | 0.995 | 0.995 | 0.99 | 0.985 | 0.98 | 0.94 | 0.98 | 0.97 | 0.965 | 0 | 0.98 | 0.975 | 0.97 | 0.98 | 0.98 | 0.98 | 0.97 | 0.99 | 0.95 | 0 | 0.97
-2%
MECC limits the degradation within 2%
-1%
Low MPKI
-2%
Med MPKI
-3%
High MPKI

## Slide 21: Power Saving in IDLE Mode
Chart: Refresh Power
| Baseline | MECC
Refresh | 1 | 0.0625
Chart: Idle Power
| Baseline | MECC
Background | 0.5 | 0.5
Refresh | 0.5 | 0.03125
16X
50%
MECC saves idle power by 50%

## Slide 22: Total Energy Savings
Chart: Total System Energy
| Baseline | MECC
Acitve | 0.65 | 0.65
Idle | 0.35 | 0.2
15%
MECC saves total energy by 15%

## Slide 23: ECC-Upgrade
Active
Idle
ECC-Upgrade
DRAM Chips
ECC
Encoder
Data + ECC-1
Data + ECC-6
ECC
Decoder
Lines
Can we enhance the ECC-Upgrade?
Entire Memory

## Slide 24: Memory downgrade tracking (MDT)
1
0
Address
Index
Need ECC-Upgrade
Don’t Need ECC-Upgrade
Chart: Memory Downgrade Tracking
| povray | tonto | wrf | gamess | hmmer | sjeng | h264ref | namd | gobmk | gromacs | perl | astar | bzip2 | dealII | soplex | cactus | calculix | gcc | zeusmp | omnetpp | sphinx | milc | xalanc | leslie | libq | Gems | lbm | bwaves | ALL
Tracer-1K | 11 | 16 | 28 | 18 | 12 | 180 | 19 | 38 | 48 | 28 | 150 | 40 | 24 | 36 | 110 | 450 | 64 | 48 | 420 | 110 | 50 | 450 | 80 | 90 | 30 | 750 | 432 | 400 | 128
MDT avoids unnecessary ECC-Upgrades
128MB

## Slide 25: Frequent transition of ECC states
Active
Idle
ECC-Downgrade
Can we enhance the ECC-Downgrade?
courtesy: Samsung, Bluetooth, Facebook, Twitter
Frequent Transition

## Slide 26: Selective memory downgrade (SMD)
Memory Activity
(MPKC)
> THLD?
Enable
ECC-Downgrade
Disable
ECC-Downgrade
Yes
No
Chart: Selective Memory Downgrade
| bwaves | lbm | Gems | libq | leslie | xalanc | milc | sphinx | omnetpp | zeusmp | gcc | calculix | cactus | soplex | dealII | bzip2 | astar | perl | gromacs | gobmk | namd | h264ref | sjeng | hmmer | povray | tonto | wrf | gamess
ECC-Downgrade Disabled | 0.2 | 0.4 | 0.6 | 0.8 | 1 | 1.2 | 1.4 | 1.6 | 1.8 | 2 | 2.2 | 2.4 | 2.6 | 2.8 | 3 | 6 | 8 | 10 | 12 | 38 | 45 | 100 | 100 | 100 | 100 | 100 | 100 | 100
ECC-Downgrade Enabled | 99.8 | 99.6 | 99.4 | 99.2 | 99 | 98.8 | 98.6 | 98.4 | 98.2 | 98 | 97.8 | 97.6 | 97.4 | 97.2 | 97 | 94 | 92 | 90 | 88 | 62 | 55 | 0 | 0 | 0 | 0 | 0 | 0 | 0
SMD avoids frequent transition of ECCs
Low MPKI

## Slide 27: Executive Summary
Energy consumption determines the usability of emerging mobile computing devices
DRAM refresh operations accounts for significant fraction of memory system’s energy
Results: -50% idle power, -15% overall energy, with only 2% performance degradation
 | Strong ECC | Weak ECC
Active Mode (refresh power negligible) | Bad Performance | Good Performance
Idle Mode (performance not critical) | Huge Energy Savings | No Energy Saving
Morphable ECC

## Slide 28: Reducing Refresh Power in Mobile Devices with Morphable ECC
Chiachen Chou, Georgia Tech
Prashant Nair, Georgia Tech
Moinuddin K. Qureshi, Georgia Tech
DSN-45
06/24/2015
Rio de Janeiro, Brazil
Computer Architecture and Emerging Technologies Lab, Georgia Tech

## Slide 29: Error correction code (ECC)
ECC: tolerate refresh errors
Q: how many errors should the system tolerate?
ECC-1
ECC-6
64B cache line
✘
Not OK
✔
Good
Correct: 5 refresh+1 soft
Refresh rate of 1s needs ECC-6 for errors
Notes: We can use error correction code to tolerate the errors.
The question is how many error should be tolerated?
We first denote the strength of ECC
If the error correction code can correct K errors in a range, it is referred to as ECC-K.
Typically, for memory system, ECC works on a 64B cache line.
Given the refresh rate is 1s, and the bit error rate is 10^-4,
#@ we found that the ECC strength has to at least ECC-5 for the system to be functional.
Thus, we use ECC-6 to provision the extra protection for soft errors
However, using ECC-6 has some drawbacks.

## Slide 30: How to reduce Refresh Operations?
Option 1
  Restore memory content into non-volatile storage
Option 2
  Reduce refresh rate
✘
Long Transfer Latency (few tens seconds)
✘
Slow Response Time (bad user experience)

## Slide 31: MECC: Overview
MECC uses two ECC based on modes
Notes: During the active mode, the system uses normal refresh rate and accesses memory with the latency of weak ECC.
When the system becomes idle, we convert weak ECC to strong ECC.
We call this conversion from weak ECC to strong ECC ECC-Upgrade .
Once the memory is upgraded, the memory is transitioned into self refresh mode, but with a refresh rate of 1s.
Thus, in the idle period, the refresh operations get reduced by 16x.
When the system is activated, the memory refresh rate is increased to 64ms.
The first access to a line gets the line in strong-ECC state;
however this line is then converted to weak-ECC state and written back to memory.
The conversion from strong ECC to weak ECC is referred to as ECC-Downgrade .
This conversion ensures that subsequent memory request to the same data block would not pay the latency overheads of strong ECC;
Therefore in the active mode the common-case latency overhead becomes that of weak ECC.
Note that lines undergo ECC-Downgrade on a demand basis, which avoids wasteful transitions of ECC status for unused lines.
#@ Thus, MECC uses two ECC based on the system’s mode.

## Slide 32: MECC: Design
Memory controller uses ECC-mode bits to decode with different ECC
Notes: In order to support MECC, we need some modification to the DRAM memory controller.
We of course need ECC encoder and ECC decoder to be able to use ECC.
However, we need the encoder and the decoder for both weak and strong ECC.
In our case, we choose ECC-1, and ECC-6.
When a line is accessed in the active mode, the memory controller needs to know which decoder should be employed to decode the line.
#@ To provide this information, the line is appended with status bit called ECC-mode .
When ECC-mode is 0, the line is decoded with weak ECC.
and when it is 1, the line is decoded with strong ECC.
Also, MECC also relies on support from the memory device to change the refresh frequency in idle mode,
We use an internal counter, which would be incremented on each refresh pulse
The outgoing refresh pulse is sent to the DRAM array only on counter overflow.
To support 1s refresh rate, we need a 4-bit counter.

## Slide 33: MECC: ECC storage
Notes: MECC relies on having the ECC code (for both ECC-1and ECC-6) stored in the DRAM arrays
Current DDR generations typically do not have ECC capability.
However, future DRAM generations, including DDR4, LPDDR4, are equipped with ECC capability to tolerate failure in small technology node.
We assume that the baseline mobile memory system supports ECC.
Now let’s see how we can store both weak ECC and strong ECC in DRAM without requiring any additional storage.
We propose to have both SECDED and ECC-6 on a line size granularity (64 bytes).
For SECDED, we would need 11 bits, and for ECC-6 we would need 60 bits
Note that, we would not need storage for both SECDED and ECC-6 at the same time, as the line can either be using SECDED or ECC-6.
Thus, we need at most 60 bits for MECC.
Given the DRAM equipped with ECC has 64 bits reserved for ECC.
We propose to use all the 64 bits in conjunction to repair the entire line.
The first four bits in this 64 bit ECC space is ECC-mode bits, implemented with 4-way redundancy for fault tolerance.
The remaining 60 bits are used for either SECDED or ECC-6.
Thus, MECC can be implemented easily with a memory system that supports the traditional (72,64) code,
without the need of any modification to existing storage array.

## Slide 34: What is the ideal case?
 | Weak ECC | Strong ECC | Ideal
Active Mode (refresh power negligible) | Performance | Performance | Performance
Idle Mode (performance not critical) | Energy Savings | Energy Savings | Energy Savings
✔
✔
✔
✔
✘
✘