## Slide 1: FLEXclusion: Balancing Cache Capacity and On-chip Bandwidth via Flexible Exclusion
Jaewoong Sim Jaekyu Lee
Moinuddin K. Qureshi Hyesoon Kim

## Slide 2: Outline
Motivation
FLEXclusion
  Design
  Monitoring & Operation
  Extension
Evaluations
Conclusion

## Slide 3: Introduction
Today’s processors have multi-level cache hierarchies
  Design options for each size, inclusion property, # of levels, ...
Design choice for cache inclusion
  Inclusion: upper-level cache blocks always exist in the lower-level cache
  Exclusion: upper-level cache blocks must not exist in the lower-level cache
  Non-Inclusion : may contain the upper-level cache blocks
Inclusion
Exclusion
Non-inclusion
UPPER-LEVEL
LOWER-LEVEL

## Slide 4: Trend of Cache Size Ratio
Trend of total non-LLC capacity to LLC capacity
  High ratio indicates more data duplications with inclusion/non-inclusions
Chart: Year
| 2001 | 2001 | 2001 | 2001 | 2002 | 2004 | 2005 | 2006 | 2006 | 2006 | 2007 | 2007 | 2008 | 2008 | 2008 | 2009 | 2009 | 2010 | 2010 | 2010 | 2010 | 2011 | 2011 | 2011 | 2011 | 2011 | 2011
Non-LLC to LLC Ratio | 0.125 | 0.125 | 0.0625 | 0.125 | 0.0625 | 0.03125 | 0.015625 | 0.015625 | 0.015625 | 0.03125 | 0.03125 | 0.0625 | 0.041667 | 0.020833 | 0.125 | 0.125 | 0.125 | 0.125 | 0.125 | 0.125 | 0.125 | 0.125 | 0.16667 | 0.1 | 0.16667 | 0.125 | 0.1
Ratio of non-LLC to LLC sizes of Intel’s processors over the past 10 years
Multi-Core Era Begins
L2: 4 x 256KB , L3: 6MB L3
More than 15% duplication!!
More Duplication
For Capacity: Exclusion is a better option

## Slide 5: On-Chip Traffic
What about on-chip traffic?
  Each design also has a different impact on on-chip traffic
DRAM
L2
L3 (LLC)
Non-Inclusive Hierarchy
Clean Victim
Dirty Victim
Fill Flow
L3 Hit
L2
L3 (LLC)
Exclusive Hierarchy
Clean Victim
Dirty Victim
Fill Flow
L3 Hit
For Bandwith: Non-Inclusion is a better option
More Traffic!!
DRAM
Sliently
Dropped!

## Slide 6: Static Inclusion
Chart: Performance of Exclusion Relative to Non-Inclusion
| 1.1346733668341711 | 1.129445234708393 | 1.2512562814070349 | 1.128111718275653 | 1.025202520252025 | 1.017937219730942 | 1.0210526315789481 | 1.0600706713780921 | 0.99808061420345495 | 1.028720626631854 | 1.0726495726495731 | 1.0172839506172839 | 1.017786561264822
bzip2 | 3.3756 | 3.7044 | 0.10689 | 1.1706 | 1.2582 | 1.4822 | 51.9754 | 12.1906 | 23.0106 | 26.507 | 25.8157 | 17.5206 | 18.7584
want to go for non-inclusion
want to go for exclusion
  Question: Which design do we want to choose?
More performance benefits on exclusion
More BW consumption on exclusion

## Slide 7: Static Inclusion : Problem
Each policy has its advantages/disadvantages
  Non-Inclusion provides less capacity but higher efficiency on on-chip traffic
  Exclusion provides more capacity but low efficiency on on-chip traffic
Workloads have diverse capacity/bandwidth requirement
Problem: No single static cache configuration works best for all workloads 

## Slide 8: Our Solution : Flexible Exclusion
Dynamically change cache inclusion according to the workload requirement!

## Slide 9: Our Solution : Flexible Exclusion
Providing both non-inclusion and exclusion
  Capture the best of capacity/bandwidth requirement
Key Observation
  Non-inclusion and exclusion require similar hardware
Benefits of FLEXclusion
  Reducing on-chip traffic compared to exclusion
  Improving performance compared to non-inclusion

## Slide 10: Outline
Motivation
FLEXclusion
  Design
  Monitoring & Operation
  Extension
Evaluations
Conclusion

## Slide 11: FLEXclusion Overview
Goal: Adapts cache inclusion between non-inclusion and exclusion
Overall Design
  Monitoring logic
  A few logic blocks in the hardware to control traffic

## Slide 12: Design
  EXCL-REG: to control L2 clean victim data flow
  NICL-GATE: to control incoming blocks from memory
  Monitoring & policy decision logic: to switch operating mode
Last-Level Cache
L2 Cache
EXCL-REG
Policy Decision & Information Collection
Logic
L3 Line Fill
NICL-GATE
L2 Line Fill
L2 Clean Victim
Monitoring logic is required in many modern cache mechanisms!

## Slide 13: Non-inclusive Mode (PDL signals 0)
  Clean L2 victims are silently dropped
  Incoming blocks are installed into both L2 and L3
  L3 hitting blocks keep residing in the cache
Last-Level Cache
L2 Cache
EXCL-REG
Policy Decision & Information Collection
Logic
L3 Line Fill
NICL-GATE
L2 Line Fill
L2 Clean Victim
Non-inclusive mode follows typical non-inclusive behavior

## Slide 14: Exclusive Mode (PDL signals 1)
  Clean L2 victims are inserted into L3
  Incoming blocks are only installed into L2
  L3 hitting blocks are invalidated
Last-Level Cache
L2 Cache
EXCL-REG
Policy Decision & Information Collection
Logic
L3 Line Fill
NICL-GATE
L2 Line Fill
L2 Clean Victim
Performs similar to typical exclusive design except for L3 insertions from L2

## Slide 15: Requirement Monitoring
Set-dueling method is used to capture
  performance and traffic behavior of exclusion and non-inclusion
Sampling sets follow their original behavior
Monitor cache miss and insertion
Other sets follow the winning policy
Counters
Set 0
Set 1
Set 2
Set 3
Set 4
Set 5
Set 6
Set 7
Non-Inclusive Set
Exclusive Set
Following Set
Cache Miss
Insertion
Cache Miss
Insertion
PDL
LLC
L2
ICL

## Slide 16: Operating Region
Decision of winning policy is made by Policy Decision Logic (PDL)
  Basic operating mode is determined by Perfth
  Extensions of FLEXclusion use Insertionth for further performance/traffic optimization
PDL
LLC
L2
ICL
L3 IPKI
Difference
1.0
Perfth
Insertionth
Non-Inclusive Region
Exclusive Region
Non-Inclusive Region
(Aggressive)
Exclusion Performance Relative
to Non-Inclusion (Cache Miss)
Exclusive Region
(Bypass)
Miss(NICL) – Miss(EX) > Perfth
Ins(EX) – Ins(NICL) > Insertionth

## Slide 17: Extensions of FLEXclusion
  Per-core policy: to isolate each application behavior
  Aggressive non-inclusion: to improve performance in non-inclusive mode
  Bypass on exclusive mode: to reduce traffic in exclusive mode
L2
LLC
Line Fill
(DRAM)
Hit on LLC
Clean Victim
Bypass on exclusive mode
L2
LLC
Line Fill
(DRAM)
Hit on LLC
Clean Victim
Aggressive non-inclusive mode
Detail explanations are in the paper.

## Slide 18: FLEXclusion Operation
A FLEXclusive cache changes operating mode at run-time
  FLEXclusion does not require any special actions
- On a switch from non-inclusive to exclusive mode
- On a switch from exclusive to non-inclusive mode
FLEXclusion Mode
Non-Inclusive
Exclusive
Non-Inclusive
L2
LLC
FLEXclusive Hierarchy
FILL
FILL
Dirty
Evict
Evict
Written back into the same position!
Hit
Evict
Hit
Dirty
Evict

## Slide 19: Outline
Motivation
FLEXclusion
  Design
  Monitoring & Operation
  Extension
Evaluations
Conclusion

## Slide 20: Evaluations
MacSim Simulator
  A cycle-level in house simulator (now public)
  Power results with Orion (Wang+[MICRO’02])
Baseline Processor
  4-core, 4.0GHz, private L1 and L2, shared L3
Workloads
  Group A: bzip2, gcc, hmmer, h264, xalancbmk, calculix (Low MPKI)
  Group B: mcf, omnetpp, bwaves, soplex, lesilie3d, wrf, sphinx3 (High MPKI)
  Multi-programmed: 2-MIX-S, 2-MIX-A, 4-MIX-S
Other results in the paper
  Multi-programmed workloads, per-core, aggressive mode, bypass, threshold sensitivity

## Slide 21: Evaluations – Performance/Traffic
Chart: L3 IPKI Normalized to Non-Inclusion
| 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | bzip2 | gcc | hmmer | h264ref | xalancbmk | calculix | mcf | omnetpp | bwaves | leslie3d | soplex | wrf | sphinx3 | AVG.
Exclusion | 5.7146 | 5.7138 | 5.7124 | 5.138 | 5.1397 | 5.1782 | 1.0343 | 1.0313 | 1.0309 | 4.8655 | 4.8188 | 4.8158 | 2.3754 | 2.3742 | 2.3436 | 3.1538 | 3.1533 | 3.1534 | 4.7339 | 4.7335 | 4.7337 | 2.7919 | 2.7949 | 2.799 | 34.278 | 34.278 | 34.2783 | 5.2859 | 5.3089 | 5.2166 | 3.7756 | 3.7479 | 3.7464 | 3.1265 | 3.0991 | 3.1456 | 24.4511 | 24.6168 | 23.6642 | 4.5571 | 4.5471 | 4.5456
FLEXclusion | 5.4277 | 1.5993 | 1.0359 | 4.9356 | 1.0648 | 1.0592 | 1.0322 | 1.0005 | 1.0001 | 4.59 | 1.0549 | 1.0248 | 2.2489 | 2.2119 | 1.3275 | 1.3439 | 1.0332 | 1.4485 | 1.1096 | 1.0584 | 1.029 | 2.6949 | 1.1744 | 1.0118 | 1.52 | 6.8239 | 1.26 | 1.0661 | 1.0666 | 1.0327 | 3.6845 | 3.6189 | 1.0212 | 1.0322 | 2.7748 | 1.0158 | 1.3697 | 24.0456 | 14.3017 | 1.9244 | 2.2465 | 1.2445
Chart: Performance Relative to Exclusion
| 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | 1MB | 2MB | 4MB | bzip2 | gcc | hmmer | h264ref | xalancbmk | calculix | mcf | omnetpp | bwaves | leslie3d | soplex | wrf | sphinx3 | AVG.
Non-Inclusion | 0.88131 | 0.98638 | 0.99851 | 0.88539 | 0.97983 | 0.99423 | 0.7992 | 0.98031 | 1.0028 | 0.88644 | 0.998 | 1.0005 | 0.97542 | 0.97821 | 0.99127 | 0.98238 | 0.99415 | 0.97894 | 0.97938 | 0.98 | 0.98131 | 0.94333 | 0.95413 | 0.9673 | 1.0019 | 0.99427 | 1 | 0.97208 | 0.98254 | 0.99506 | 0.93227 | 0.92632 | 0.95536 | 0.98301 | 0.93304 | 0.97206 | 0.98252 | 0.93023 | 0.83902 | 0.937 | 0.97025 | 0.97414
FLEXclusion | 0.99557 | 0.98558 | 0.99851 | 0.99496 | 0.97983 | 0.99192 | 0.99063 | 0.98088 | 1.0022 | 0.99139 | 0.998 | 1.0005 | 0.99561 | 0.99581 | 0.99127 | 0.98752 | 0.99415 | 0.98302 | 0.97938 | 0.98 | 0.98131 | 0.99667 | 0.95719 | 0.97003 | 1.0019 | 1.0019 | 1 | 0.97208 | 0.98254 | 0.99506 | 1 | 0.99649 | 0.95536 | 0.98301 | 0.98884 | 0.97206 | 0.98252 | 0.99821 | 0.95638 | 0.99006 | 0.98758 | 0.98431
Performance
Traffic
FLEXclusion performs similar to exclusion
AVG. 6.3% loss for 1MB
5.9% improvement over non-inclusion!!
72.6% reduction over exclusion!!

## Slide 22: Evaluations - Effective Cache Size
Running the same benchmark on 1-/2-/4- cores (4MB L3)
Chart: 
| bzip | gcc | hmmer | h264 | xalancbmk | calculix | mcf | omentpp | bwaves | leslie3d | soplex | wrf | sphinx3 | AVG.
Non-Inclusive Mode (1-Core) | 70140 | 84448 | 31521 | 26608 | 31257 | 26371 | 1104412 | 293742 | 436189 | 581141 | 566211 | 406436 | 136938 | 3795414
Exclusive Mode (1-Core) | 0 | 0 | 0 | 0 | 0 | 9482 | 0 | 0 | 0 | 0 | 0 | 0 | 319589 | 329071
Chart: 
| bzip | gcc | hmmer | h264 | xalancbmk | calculix | mcf | omentpp | bwaves | leslie3d | soplex | wrf | sphinx3 | AVG.
Non-Incluive Mode (2-Cores) | 70241 | 169911 | 63203 | 30842 | 7610 | 70746 | 2276222 | 307411 | 717969 | 1098468 | 50256 | 578730 | 6545 | 5448154
Exclusive Mode (2-Cores) | 1 | 0 | 0 | 32692 | 62986 | 0 | 0 | 319723 | 157666 | 0 | 1306231 | 252583 | 774536 | 2906418
Chart: 
| bzip | gcc | hmmer | h264 | xalancbmk | calculix | mcf | omentpp | bwaves | leslie3d | soplex | wrf | sphinx3 | AVG.
Non-Inclusive Mode (4-Cores) | 18844 | 10239 | 5040 | 6331 | 14865 | 143597 | 4949556 | 11833 | 1762146 | 2244546 | 38701 | 1629976 | 1442808 | 12278482
Exclusive Mode (4-Cores) | 355385 | 436546 | 186635 | 128717 | 119923 | 0 | 56149 | 1272863 | 0 | 0 | 2482582 | 0 | 0 | 5038800
One thread is enjoying the cache!!
Threads are competing for shared caches!!
FLEXclusive cache is configured as exclusive mode more often!!
FLEXclusion adapts inclusion on the effective cache size for each workload!!

## Slide 23: Evaluations – Traffic & Power
Impact on L3 insertion traffic reduction in total?
  FLEXclusion effectively reduces the traffic
Chart: Traffic Normalized to Exclusion
| Exclusion | FLEXclusion | Non-Inclusion | Exclusion | FLEXclusion | Non-Inclusion | Exclusion | FLEXclusion | Non-Inclusion | Exclusion | FLEXclusion | Non-Inclusion | Exclusion | FLEXclusion | Non-Inclusion | Exclusion | FLEXclusion | Non-Inclusion | Exclusion | FLEXclusion | Non-Inclusion | Exclusion | FLEXclusion | Non-Inclusion | Exclusion | FLEXclusion | Non-Inclusion | Exclusion | FLEXclusion | Non-Inclusion | Exclusion | FLEXclusion | Non-Inclusion | Exclusion | FLEXclusion | Non-Inclusion | Exclusion | FLEXclusion | Non-Inclusion | Exclusion | FLEXclusion | Non-Inclusion | bzip2 | gcc | hmmer | h264 | xalancbmk | calculix | mcf | omnetpp | bwaves | leslie3d | soplex | wrf | sphinx3 | AVG. | Single-threaded (A+B)
Address | 0.057372 | 0.058026 | 0.057692 | 0.067811 | 0.067885 | 0.067789 | 0.056502 | 0.055871 | 0.055823 | 0.060836 | 0.058912 | 0.058325 | 0.081664 | 0.079736 | 0.079649 | 0.082823 | 0.080838 | 0.081012 | 0.091854 | 0.095796 | 0.095825 | 0.083513 | 0.083703 | 0.083725 | 0.11192 | 0.11129 | 0.11128 | 0.095229 | 0.092563 | 0.092587 | 0.07866 | 0.08004 | 0.080064 | 0.085986 | 0.083331 | 0.083361 | 0.069716 | 0.066005 | 0.069695 | 0.087277 | 0.087514 | 0.087792
Data (L2->L3) | 0.46762 | 0.094794 | 0.082555 | 0.44157 | 0.10557 | 0.093094 | 0.46585 | 0.45551 | 0.45507 | 0.4571 | 0.10011 | 0.088661 | 0.40338 | 0.18882 | 0.1816 | 0.42227 | 0.22635 | 0.13565 | 0.3796 | 0.11058 | 0.098942 | 0.38996 | 0.1728 | 0.16393 | 0.36034 | 0.029967 | 0.014675 | 0.36168 | 0.10055 | 0.089009 | 0.41973 | 0.13509 | 0.12439 | 0.37558 | 0.14245 | 0.13364 | 0.41686 | 0.32338 | 0.02183 | 0.38943 | 0.136 | 0.1028
Data (L3->L2) | 0.43333 | 0.43217 | 0.43506 | 0.34128 | 0.35654 | 0.3575 | 0.44692 | 0.45202 | 0.45245 | 0.41688 | 0.41101 | 0.4163 | 0.17477 | 0.16599 | 0.16658 | 0.15273 | 0.1545 | 0.15293 | 0.099965 | 0.075173 | 0.074917 | 0.16207 | 0.16929 | 0.1691 | 0.019369 | 0.0068811 | 0.0070085 | 0.082392 | 0.0986 | 0.098386 | 0.23307 | 0.21295 | 0.21275 | 0.12343 | 0.089303 | 0.08901 | 0.39839 | 0.44385 | 0.41065 | 0.158 | 0.14942 | 0.14691
Data (MC<->Caches) | 0.041682 | 0.045492 | 0.04249 | 0.14933 | 0.15413 | 0.15356 | 0.030727 | 0.025484 | 0.024902 | 0.065175 | 0.059597 | 0.054312 | 0.34018 | 0.35481 | 0.35462 | 0.34217 | 0.35376 | 0.36004 | 0.42858 | 0.48609 | 0.48683 | 0.36445 | 0.39013 | 0.39114 | 0.50837 | 0.5119 | 0.51177 | 0.4607 | 0.44339 | 0.44386 | 0.26854 | 0.32832 | 0.32986 | 0.41501 | 0.43502 | 0.43559 | 0.11503 | 0.076736 | 0.1109 | 0.36529 | 0.38973 | 0.39283
Chart: Benchmarks
| A+B | 2-MIX-S | 4-MIX-S | 2-MIX-A
Exclusion | 1 | 1 | 1 | 1
FLEXclusion | 0.8043 | 0.8441 | 0.82371 | 0.7947
Non-Inclusion | 0.77983 | 0.74463 | 0.73965 | 0.69087
20% Reduction
L3 Insertion takes up more than 40%!
Reduced to ~10% with FLEXclusion!!

## Slide 24: Outline
Motivation
FLEXclusion
  Design
  Monitoring & Operation
  Extension
Evaluations
Conclusion

## Slide 25: Conclusions & Future Work
  FLEXclusion balances performance and on-chip bandwidth consumption
    depending on the workload requirement
    with negliglibe hardware changes
  5.9% performance improvement over non-inclusion
  72.6% L3 insertion traffic reduction over exclusion (20% power reduction)
Future Work
  More generic flexclusion including inclusion property
  Impact on on-chip network

## Slide 26: Q/A
Thank you!