## Slide 1: ArchShield: Architectural Framework for Assisting DRAM Scaling By Tolerating High Error-Rates
Prashant Nair
Dae-Hyun Kim
Moinuddin K. Qureshi

## Slide 2
DRAM: Basic building block for main memory for four decades
DRAM scaling provides higher memory capacity. Moving to smaller node provides ~2x capacity
Shrinking DRAM cells becoming difficult  threat to scaling
Efficient error handling can help DRAM technology scale
Introduction
Technology node (smaller )
Efficient Error
Mitigation
Scaling (Feasibility)

## Slide 3
Scaling is difficult. More so for DRAM cells.
Volume of capacitance must remain constant (25fF)
Scaling: 0.7x dimension, 0.5x area  2x height
With scaling, DRAM cells not only become narrower but longer
Why DRAM Scaling is Difficult?

## Slide 4
DRAM: Aspect Ratio Trend
Narrow cylindrical cells are mechanically unstable  breaks

## Slide 5
Unreliability of ultra-thin dielectric material
In addition, DRAM cell failures also from:
  Permanently leaky cells
  Mechanically unstable cells
  Broken links in the DRAM array
Permanent faults for future DRAMs expected to be much higher
(we target an error rate as high as 100ppm)
More Reasons for DRAM Faults
Q
Charge
Leaks
DRAM
Cell Capacitor
Permanently
Leaky Cell
Mechanically
Unstable Cell
DRAM Cell Capacitor
(tilting towards ground)
Broken Links
DRAM Cells

## Slide 6
Introduction
Current Schemes
ArchShield
Evaluation
Summary
Outline

## Slide 7
DRAM chip (organized into rows and columns) have spares
Laser fuses enable spare rows/columns
Entire row/column needs to be sacrificed for a few faulty cells
Row and Column Sparing Schemes have large area overheads
Row and Column Sparing
DRAM Chip:
Before Row/Column Sparing
Spare Rows
Spare Columns
Faults
Replaced Rows
DRAM Chip:
After Row/Column Sparing
Replaced Columns
Deactivated Rows
and Columns

## Slide 8
Commodity ECC DIMM with SECDED at 8 bytes (72,64)
Mainly used for soft-error protection
For hard errors, high chance of two errors in same word (birthday paradox)
For 8GB DIMM  1 billion words
Expected errors till double-error word
= 1.25*Sqrt(N) = 40K errors  0.5 ppm
SECDED not enough for high error-rate (+ lost soft-error protection)
Commodity ECC-DIMM

## Slide 9
Strong ECC (BCH) codes are robust, but complex and costly
Each memory reference incurs encoding/decoding latency
For BER of 100 ppm, we need ECC-4  50% storage overhead
Strong ECC codes provide an inefficient solution for tolerating errors
Strong ECC Codes
Memory Controller
Strong ECC
Encoder
+
Decoder
DRAM Memory System
Memory
Requests
Memory
Requests
Notes: Strong ECC
ArchShield
How it works
Architecture
Components

## Slide 10
Most faulty words have 1-bit error  The skew in fault probability can be leveraged to develop low cost error resilience
Dissecting Fault Probabilities
Faulty Bits per word (8B) | Probability | Num words in 8GB
0 | 99.3% | 0.99 Billion
1 | 0.007 | 7.7 Million
2 | 26 x 10-6 | 28 K
3 | 62 x 10-9 | 67
4 | 10-10 | 0.1
At Bit Error Rate of 10-4 (100ppm) for an 8GB DIMM (1 billion words)
Goal: Tolerate high error rates with commodity ECC DIMM while retaining soft-error resilience

## Slide 11
Introduction
Current Schemes
ArchShield
Evaluation
Summary
Outline

## Slide 12
ArchShield: Overview
ArchShield
Replication Area
Fault Map
(cached)
Fault Map
Main Memory
Inspired from Solid State Drives (SSD) to tolerate high bit-error rate
Expose faulty cell information to Architecture layer via runtime testing
ArchShield stores the error mitigation information in memory
Most words will be error-free
1-bit error handled with SECDED
Multi-bit error handled with replication

## Slide 13
ArchShield: Runtime Testing
When DIMM is configured, runtime testing is performed. Each 8B word gets classified into one of three types:
Runtime testing identifies the faulty cells to decide correction
No Error
(Information about faulty cells can be stored in hard drive for future use)
(Replication not needed)
SECDED can correct soft error
1-bit Error
SECDED can correct hard error
Need replication for soft error
Multi-bit Error
Word gets decommissioned
Only the replica is used

## Slide 14
Architecting the Fault Map
Fault Map (FM) stores information about faulty cells
Per word FM is expensive (for 8B, 2-bits or 4-bits with redundancy)  Keep FM entry per line (4-bit per 64B)
FM access method
  Table lookup with Lineaddr
Avoid dual memory access via
  Caching FM entries in on-chip LLC
  Each 64-byte line has 128 FM entries
  Exploits spatial locality
Fault Map – Organized at Line
Granularity and is also cachable
Line-Level Fault Map + Caching provides low storage and low latency
Main Memory
Replication Area
Faulty Words
Replicated
Words
Fault Map

## Slide 15
Architecting Replication Area
Faulty cells replicated at word-granularity in Replication Area
Fully associative Replication Area? Prohibitive latency
Set associative Replication Area? Set overflow problem
Fully Associative Structure
Set Associative Structure
Replicated
Words
Chances of Set Overflowing!
Set 1
Set 2
Set 1
Set 2
Replication Area
Faulty Words
Fault Map
Main Memory

## Slide 16
Overflow of Set-Associative RA
There are 10s/100s of thousand of sets  Any set could overflow
How many entries used before one set overflows? Buckets-and-Balls
6-way table only 8% full when one set overflows  Need 12x entries

## Slide 17
Scalable Structure for RA
With Overflow Sets, Replication Area can handle non uniformity
OFB
OFB
16-Sets
16-overflow sets
Replication Area Entry
1
PTR
1
PTR
TAKEN BY SOME OTHER SET

## Slide 18
Replication
Area (256MB)
ArchShield: Operation
Faulty Words
Last Level Cache
R-bit
R-bit
Main Memory
Read Request
Fault Map Entry
Replicated Word
Fault Map
(64 MB)
Last Level Cache Miss!
Read Transaction
1. Query Fault Map Entry
2. Fault Map Miss
Fault Map Line
Fetch
1. Query Fault Map Entry
2. Fault Map Hit: No Faulty words
1. Query Fault Map Entry
2. Fault Map Hit: Faulty word
Read Transaction
Replication Area
Set R-Bit
Write Request
Check R-Bit
R-Bit Set, write to 2 locations
Else 1 location
OS-usable
Mem(7.7GB)

## Slide 19
Introduction
Current Schemes
ArchShield
Evaluation
Summary
Outline

## Slide 20
Experimental Evaluation
Configuration:
8-core CMP with 8MB LLC (shared)
8GB DIMM, two channels DDR3-1600
Workloads: SPEC CPU 2006 suite in rate mode
Assumptions: Bit error rate of 100ppm (random faults)
Performance Metric: Execution time norm to fault free baseline

## Slide 21
Chart: High MPKI
| mcf | lbm | soplex | milc | libquantum | omnetpp | bwaves | gcc | sphinx3 | GemsFDTD | leslie3d | wrf | cactusADM | zeusmp | bzip2 | dealII | xalancbmk | hmmer | perlbench | h264ref | astar | gobmk | gromacs | sjeng | namd | tonto | calculix | gamess | povray | Gmean
ArchShield (No FM Traffic) | 1.01 | 1.029 | 1.011 | 1.016 | 1.007 | 1.016 | 1.005 | 1.017 | 1.005 | 1.019 | 1.01 | 1.012 | 1.008 | 1.01 | 1.007 | 1.002 | 1.005 | 1.013 | 1.001 | 1 | 1 | 1.001 | 1.002 | 1 | 1 | 1 | 1 | 1 | 1 | 1.007
ArchShield (No Replication Area) | 1.033 | 1 | 1.004 | 1.003 | 1.006 | 1.057 | 1.006 | 1 | 1.012 | 1.001 | 1.001 | 1 | 1.002 | 1.002 | 1.013 | 1.002 | 1.006 | 1.013 | 1.007 | 1.005 | 1.009 | 1.006 | 1.001 | 1.004 | 1 | 1 | 1 | 1 | 1 | 1.006
ArchShield | 1.042 | 1.025 | 1.015 | 1.017 | 1.013 | 1.069 | 1.01 | 1.015 | 1.015 | 1.019 | 1.011 | 1.013 | 1.009 | 1.011 | 1.022 | 1.006 | 1.011 | 1.013 | 1.008 | 1.008 | 1.01 | 1.006 | 1.003 | 1.004 | 1 | 1 | 1 | 1 | 1 | 1.013
Execution Time
On average, ArchShield causes 1% slowdown
Low MPKI
Two sources of slowdown:
Fault Map access and Replication Area access

## Slide 22
Chart: 
| mcf | lbm | soplex | milc | libquantum | omnetpp | bwaves | gcc | sphinx3 | GemsFDTD | leslie3d | wrf | cactusADM | zeusmp | bzip2 | dealII | xalancbmk | hmmer | perlbench | h264ref | astar | gobmk | gromacs | sjeng | namd | tonto | calculix | gamess | povray | Average
 | 0.909 | 0.987 | 0.98 | 0.942 | 0.985 | 0.819 | 0.985 | 0.98 | 0.965 | 0.944 | 0.984 | 0.985 | 0.986 | 0.985 | 0.977 | 0.983 | 0.86 | 0 | 0.992 | 0.92 | 0.972 | 0.988 | 0.925 | 0.986 | 0.508 | 0.979 | 0.98 | 0.971 | 0.981 | 0.963 | 0 | 0.946
Fault Map Hit-Rate
Hit rate of Fault Map in LLC is high, on average 95%
High MPKI
Low MPKI
Hit-Rate

## Slide 23
Analysis of Memory Operations
Only 1.2% of the total accesses use the Replication Area
Fault Map Traffic accounts for <5 % of all traffic
Transaction | 1 Access(%) | 2 Access (%) | 3 Access (%)
Reads | 72.1 | 0.02 | ~0
Writes | 22.1 | 1.2 | 0.05
Fault Map | 4.5 | N/A | N/A
Overall | 98.75 | 1.2 | 0.05

## Slide 24
Comparison With Other Schemes
The read-before-write of Free-p + strong ECC  high latency
ECC-4 incurs decoding delay
The impact of execution time is minimum in ArchShield
Chart: High MPKI
| mcf | lbm | soplex | milc | libquantum | omnetpp | bwaves | gcc | sphinx3 | GemsFDTD | leslie3d | wrf | cactusADM | zeusmp | bzip2 | dealII | xalancbmk | hmmer | perlbench | h264ref | astar | gobmk | gromacs | sjeng | namd | tonto | calculix | gamess | povray | Gmean
FREE-p | 1.123 | 1.293 | 1.135 | 1.205 | 1.089 | 1.198 | 1.06 | 1.237 | 1.054 | 1.213 | 1.137 | 1.154 | 1.104 | 1.122 | 1.103 | 1.036 | 1.135 | 1.051 | 1.011 | 1.018 | 1.013 | 1.01 | 1.024 | 1.008 | 1 | 1 | 1 | 1 | 1 | 1.084
ECC-4 | 1.067 | 1.14 | 1.077 | 1.102 | 1.072 | 1.095 | 1.052 | 1.117 | 1.045 | 1.097 | 1.068 | 1.075 | 1.049 | 1.058 | 1.054 | 1.023 | 1.068 | 1.024 | 1.011 | 1.011 | 1.01 | 1.007 | 1.014 | 1.006 | 1 | 1 | 1 | 1 | 1 | 1.046
ArchShield | 1.042 | 1.025 | 1.015 | 1.017 | 1.013 | 1.069 | 1.01 | 1.015 | 1.015 | 1.019 | 1.011 | 1.013 | 1.009 | 1.011 | 1.022 | 1.006 | 1.011 | 1.013 | 1.008 | 1.008 | 1.01 | 1.006 | 1.003 | 1.004 | 1 | 1 | 1 | 1 | 1 | 1.013
Low MPKI
FREE-p
ECC-4
ArchShield

## Slide 25
Introduction
Current Schemes
ArchShield
Evaluation
Summary
Outline

## Slide 26
DRAM scaling challenge: High fault rate, current schemes limited
We propose to expose DRAM errors to Architecture  ArchShield
ArchShiled uses efficient Fault Map and Selective Word Replication
ArchShield handles a Bit Error Rate of 100ppm with less than 4% storage overhead and 1% slowdown
ArchShield can be used to reduce DRAM refresh by 16x (to 1 second)
Summary

## Slide 27
Questions

## Slide 28: Monte Carlo Simulation
Probability that a structure is unable to handle given number of errors (in million). We recommend the structure with 16 overflow sets to tolerate 7.74 million errors in DIMM.

## Slide 29: ArchShield FlowChart
Entries in bold are frequently accessed

## Slide 30: Memory System with ArchShield

## Slide 31: Memory Footprint

## Slide 32: ArchShield compared to RAIDR