## Slide 1
Moinuddin K. Qureshi
ECE, Georgia Tech
Gabriel H. Loh, AMD
Fundamental Latency Trade-offs in Architecting DRAM Caches
MICRO 2012

## Slide 2
3-D Memory Stacking
3-D Stacked memory can provide large caches at high bandwidth
3D Stacking for low latency and high bandwidth memory system
- E.g. Half the latency, 8x the bandwidth [Loh&Hill, MICRO’11]
Stacked DRAM: Few hundred MB, not enough for main memory
Hardware-managed cache is desirable: Transparent to software
Source: Loh and Hill MICRO’11

## Slide 3
Problems in Architecting Large Caches
Architecting tag-store for low-latency and low-storage is challenging
Organizing at cache line granularity (64 B) reduces wasted space and wasted bandwidth
Problem: Cache of hundreds of MB needs tag-store of tens of MB
E.g. 256MB DRAM cache needs ~20MB tag store (5 bytes/line)
Option 1: SRAM Tags
Fast, But Impractical
(Not enough transistors)
Option 2: Tags in DRAM
Naïve design has 2x latency
(One access each for tag, data)

## Slide 4
Loh-Hill Cache Design [Micro’11, TopPicks]
Recent work tries to reduce latency of Tags-in-DRAM approach
LH-Cache design similar to traditional set-associative cache
2KB row buffer = 32 cache lines
Speed-up cache miss detection:
A MissMap (2MB) in L3 tracks lines of pages resident in DRAM cache
Miss
Map
Data lines (29-ways)
Tags
Cache organization: A 29-way set-associative DRAM (in 2KB row) Keep Tag and Data in same DRAM row (tag-store & data store)
Data access guaranteed row-buffer hit (Latency ~1.5x instead of 2x)

## Slide 5
Cache Optimizations Considered Harmful
Need to revisit DRAM cache structure given widely different constraints
DRAM caches are slow  Don’t make them slower
Many “seemingly-indispensable” and “well-understood” design choices degrade performance of DRAM cache:
  Serial tag and data access
  High associativity
  Replacement update
Optimizations effective only in certain parameters/constraints
Parameters/constraints of DRAM cache quite different from SRAM
E.g. Placing one set in entire DRAM row  Row buffer hit rate ≈ 0%

## Slide 6: Outline
Introduction & Background
Insight: Optimize First for Latency
Proposal: Alloy Cache
Memory Access Prediction
Summary
Notes: Give a brief overview of the presentation. Describe the major focus of the presentation and why it is important.
Introduce each of the major topics.
To provide a road map for the audience, you can repeat this Overview slide throughout the presentation, highlighting the particular topic you will discuss next.

## Slide 7
Simple Example: Fast Cache (Typical)
Optimizing for hit-rate (at expense of hit latency) is effective
Consider a system with cache: hit latency 0.1 miss latency: 1
Base Hit Rate: 50% (base average latency: 0.55)
Opt A removes 40% misses (hit-rate:70%), increases hit latency by 40%
Base Cache
Opt-A
Break Even
Hit-Rate=52%
Hit-Rate A=70%

## Slide 8
Simple Example: Slow Cache (DRAM)
Base Cache
Opt-A
Break Even
Hit-Rate=83%
Consider a system with cache: hit latency 0.5 miss latency: 1
Base Hit Rate: 50% (base average latency: 0.75)
Opt A removes 40% misses (hit-rate:70%), increases hit latency by 40%
Hit-Rate A=70%
Optimizations that increase hit latency start becoming ineffective

## Slide 9
Overview of Different Designs
Our Goal: Outperform SRAM-Tags with a simple and practical design
For DRAM caches, critical to optimize first for latency, then hit-rate

## Slide 10
What is the Hit Latency Impact?
Both SRAM-Tag and LH-Cache have much higher latency  ineffective
Consider Isolated accesses: X always gives row buffer hit, Y needs an row activation

## Slide 11
How about Bandwidth?
LH-Cache reduces effective DRAM cache bandwidth by > 4x
Configuration | Raw Bandwidth | Transfer Size on Hit | Effective Bandwidth
Main Memory | 1x | 64B | 1x
DRAM$(SRAM-Tag) | 8x | 64B | 8x
DRAM$(LH-Cache) | 8x | 256B+16B | 1.8x
DRAM$(IDEAL) | 8x | 64B | 8x
For each hit, LH-Cache transfers:
  3 lines of tags (3x64=192 bytes)
  1 line for data (64 bytes)
  Replacement update (16 bytes)

## Slide 12
Performance Potential
LH-Cache gives 8.7%, SRAM-Tag 24%, latency-optimized design 38%
8-core system with 8MB shared L3 cache at 24 cycles
DRAM Cache: 256MB (Shared), latency 2x lower than off-chip
Chart: 
| mcf_r | lbm_r | soplex_r | milc_r | omnet_r | gcc_r | bwaves_r | sphinx_r | gems_r | libqntm_r | Gmean
 | 1.259 | 1.238 | 1.079 | 1.012 | 1.19 | 1.266 | 0.984 | 1.154 | 0.989 | 0.803 | 1.087
 | 1.567 | 1.375 | 1.131 | 1.031 | 1.597 | 1.496 | 1.005 | 1.47 | 1.005 | 0.95 | 1.238
 | 1.615 | 1.59 | 1.155 | 1.075 | 1.668 | 1.718 | 1.081 | 1.78 | 1.09 | 1.341 | 1.384
Speedup(No DRAM$)
LH-Cache
SRAM-Tag
IDEAL-Latency Optimized

## Slide 13
De-optimizing for Performance
More benefits from optimizing for hit-latency than for hit-rate
LH-Cache uses LRU/DIP  needs update, uses bandwidth
LH-Cache can be configured as direct map  row buffer hits
Configuration | Speedup | Hit-Rate | Hit-Latency (cycles)
LH-Cache | 8.7% | 55.2% | 107
LH-Cache + Random Repl. | 10.2% | 51.5% | 98
LH-Cache (Direct Map) | 15.2% | 49.0% | 82
IDEAL-LO (Direct Map) | 38.4% | 48.2% | 35

## Slide 14: Outline
Introduction & Background
Insight: Optimize First for Latency
Proposal: Alloy Cache
Memory Access Prediction
Summary
Notes: Give a brief overview of the presentation. Describe the major focus of the presentation and why it is important.
Introduce each of the major topics.
To provide a road map for the audience, you can repeat this Overview slide throughout the presentation, highlighting the particular topic you will discuss next.

## Slide 15
Alloy Cache: Avoid Tag Serialization
Alloy Cache has low latency and uses less bandwidth
No dependent access for Tag and Data  Avoids Tag serialization
Consecutive lines in same DRAM row  High row buffer hit-rate
No need for separate “Tag-store” and “Data-Store”  Alloy Tag+Data
One “Tag+Data”

## Slide 16
Chart: 
| mcf_r | lbm_r | soplex_r | milc_r | omnet_r | bwaves_r | gcc_r | libqntm_r | sphinx_r | gems_r | Gmean
 | 1.393 | 1.368 | 1.035 | 0.941 | 1.52 | 0.951 | 1.624 | 1.053 | 1.761 | 0.952 | 1.226
 | 1.383 | 1.359 | 1.054 | 1.016 | 1.426 | 0.972 | 1.507 | 1.096 | 1.523 | 1.002 | 1.215
 | 1.591 | 1.551 | 1.149 | 1.071 | 1.648 | 1.066 | 1.708 | 1.303 | 1.764 | 1.081 | 1.366
 | 1.567 | 1.375 | 1.131 | 1.031 | 1.597 | 1.005 | 1.496 | 0.95 | 1.47 | 1.005 | 1.238
Performance of Alloy Cache
Alloy Cache with good predictor can outperform SRAM-Tag
Alloy+MissMap
SRAM-Tag
Alloy+PerfectPred
Alloy Cache
Speedup(No DRAM$)
Alloy Cache with no early-miss detection gets 22%, close to SRAM-Tag

## Slide 17: Outline
Introduction & Background
Insight: Optimize First for Latency
Proposal: Alloy Cache
Memory Access Prediction
Summary
Notes: Give a brief overview of the presentation. Describe the major focus of the presentation and why it is important.
Introduce each of the major topics.
To provide a road map for the audience, you can repeat this Overview slide throughout the presentation, highlighting the particular topic you will discuss next.

## Slide 18
Cache Access Models
Each model has distinct advantage: lower latency or lower BW usage
Serial Access Model (SAM) and Parallel Access Model (PAM)
Higher Miss Latency
Needs less BW
Lower Miss Latency
Needs more BW

## Slide 19
To Wait or Not to Wait?
Using Dynamic Access Model (DAM), we can get best latency and BW
Dynamic Access Model: Best of both SAM and PAM
When line likely to be present in cache use SAM, else use PAM
Memory Access
Predictor (MAP)
L3-miss
Address
Prediction =
Cache Hit
Prediction =
Memory Access
Use PAM
Use SAM

## Slide 20
Memory Access Predictor (MAP)
Proposed MAP designs simple and low latency
We can use Hit Rate as proxy for MAP: High hit-rate SAM, low PAM
Accuracy improved with History-Based prediction
History-Based Global MAP (MAP-G)
  Single saturating counter per-core (3-bit)
  Increment on cache hit, decrement on miss
  MSB indicates SAM or PAM
Table
Of
Counters
(3-bit)
Miss PC
MAC
2. Instruction Based MAP (MAP-PC)
  Have a table of saturating counter
  Index table based on miss-causing PC
  Table of 256 entries sufficient (96 bytes)

## Slide 21
Chart: 
| mcf_r | lbm_r | soplex_r | milc_r | omnet_r | bwaves_r | gcc_r | libqntm_r | sphinx_r | gems_r | Gmean
 | 1.393 | 1.368 | 1.035 | 0.941 | 1.52 | 0.951 | 1.624 | 1.053 | 1.761 | 0.952 | 1.226
 | 1.453 | 1.329 | 1.12 | 1.052 | 1.541 | 1.023 | 1.67 | 1.325 | 1.763 | 1.056 | 1.309
 | 1.535 | 1.551 | 1.144 | 1.063 | 1.548 | 1.067 | 1.674 | 1.317 | 1.763 | 1.079 | 1.35
 | 1.591 | 1.551 | 1.149 | 1.071 | 1.648 | 1.066 | 1.708 | 1.303 | 1.764 | 1.081 | 1.366
Predictor Performance
Simple Memory Access Predictors obtain almost all potential gains
Speedup(No DRAM$)
Alloy+MAP-Global
Alloy +MAP-PC
Alloy+PerfectMAP
Alloy+NoPred
Accuracy of MAP-Global: 82% Accuracy of MAP-PC: 94%
Alloy Cache with MAP-PC gets 35%, Perfect MAP gets 36.5%

## Slide 22
Hit-Latency versus Hit-Rate
Alloy Cache Improves Hit Latency greatly at small loss of Hit Rate
Latency | LH-Cache | SRAM-Tag | Alloy Cache
Average Latency (cycles) | 107 | 67 | 43
Relative Latency | 2.5x | 1.5x | 1.0x
Cache Size | LH-Cache (29-way) | Alloy Cache (1-way) | Delta Hit-Rate
256MB | 55.2% | 48.2% | 7%
512MB | 59.6% | 55.2% | 4.4%
1GB | 62.6% | 59.1% | 2.5%
DRAM Cache Hit Rate
Alloy Cache reduces hit latency greatly at small loss of hit-rate
DRAM Cache Hit Latency

## Slide 23: Outline
Introduction & Background
Insight: Optimize First for Latency
Proposal: Alloy Cache
Memory Access Prediction
Summary
Notes: Give a brief overview of the presentation. Describe the major focus of the presentation and why it is important.
Introduce each of the major topics.
To provide a road map for the audience, you can repeat this Overview slide throughout the presentation, highlighting the particular topic you will discuss next.

## Slide 24
Summary
DRAM Caches are slow, don’t make them slower
Previous research: DRAM cache architected similar to SRAM cache
Insight: Optimize DRAM cache first for latency, then hit-rate
Latency optimized Alloy Cache avoids tag serialization
Memory Access Predictor: simple, low latency, yet highly effective
Alloy Cache + MAP outperforms SRAM-Tags (35% vs. 24%)
Calls for new ways to manage DRAM cache space and bandwidth

## Slide 25
Questions
Acknowledgement:
Work on “Memory Access Prediction” done while at IBM Research.
(Patent application filed Feb 2010, published Aug 2011)

## Slide 26
Potential for Improvement
Design | Performance Improvement
Alloy Cache + MAP-PC | 35.0%
Alloy Cache + Perfect Predictor | 36.6%
IDEAL-LO Cache | 38.4%
IDEAL-LO + No Tag Overhead | 41.0%

## Slide 27
Size Analysis
Simple Latency-Optimized design outperforms Impractical SRAM-Tags!
Chart: 
| 64MB | 128MB | 256MB | 512MB | 1GB
 | 1.055 | 1.076 | 1.087 | 1.098 | 1.111
 | 1.144 | 1.19 | 1.238 | 1.266 | 1.293
 | 1.193 | 1.259 | 1.35 | 1.418 | 1.461
SRAM-Tags
Alloy Cache + MAP-PC
LH-Cache + MissMap
Proposed design provides 1.5x the benefit of SRAM-Tags
(LH-Cache provides about one-third the benefit)
Speedup(No DRAM$)

## Slide 28
How about Commercial Workloads?
Cache Size | Hit-Rate (1-way) | Hit-Rate (32-way) | Hit-Rate Delta
256MB | 53.0% | 60.3% | 7.3%
512MB | 58.6% | 63.6% | 5.0%
1GB | 62.1% | 65.1% | 3.0%
Data averaged over 7 commercial workloads

## Slide 29
Prediction Accuracy of MAP
MAP-PC

## Slide 30
What about other SPEC benchmarks?

## Slide 31
http://research.cs.wisc.edu/multifacet/papers/micro11_missmap_addendum.pdf
LH-Cache Addendum: Revised Results

## Slide 32
SAM vs. PAM