## Slide 1
DICE: Compressing DRAM Caches for Bandwidth and Capacity
Vinson Young
Prashant Nair
Moinuddin Qureshi
Notes: I am Vinson Young. This work is done with my collaborator Prashant Nair, and advisor Moinuddin Qureshi.
My working is on DICE: Compressing DRAM caches for bandwidth and capacity.

## Slide 2: MOORE’s LAW HITS BANDWIDTH WALL
Moore’s scaling encounters Bandwidth Wall
Notes: To continue moore’s law, we have been scaling the number of cores. This increases memory pressure. Memory system scaling has not kept up. Especially with today’s massively scaling workloads.
Memory vendors saw this problem, and have proposed a new memory technology to mitigate the bandwidth wall.

## Slide 3: 3D-DRAM MITIGATES BANDWIDTH WALL
3D-DRAM
Hybrid Memory Cube (HMC) from Micron,
High Bandwidth Memory (HBM) from Samsung
3D-DRAM improves bandwidth, but does not have capacity to replace conventional DIMM memory
Notes: The new memory technology uses 3D stacking and through silicon via to provide high memory bandwidth.
//To differentiate, I will refer to this kind of memory as 3D DRAM through out the talk.

## Slide 4: 3D-DRAM as a CACHE (3D-DRAM CACHE)
OS-visible Space
System Memory
3D-DRAM Cache
Memory Hierarchy
fast
slow
CPU
L1$
L2$
L3$
CPU
L2$
L1$
Architecting 3D-DRAM as a cache can improve memory bandwidth (and avoid OS/software change)
MCDRAM from Intel,
HBC from AMD
Notes: One way to use the high-bandwidth memory is to architect as a cache, between system memory and L3, to invisibly speed up applications.
Note that this type of organization is already used in today’s Intel Knights Landing MCDRAM (Multi-Channel DRAM), and AMD’s High-Bandwidth Cache.
Improving DRAM caches would have practical impacts on today’s large-scale systems.

## Slide 5: PRACTICAL 3D-DRAM CACHE: ALLOY CACHE
Practical DRAM cache: low latency and bandwidth-efficient
Tags “part-of-line”  Alloy Tag+Data  Avoid Tag Serialization
One “Tag+Data”
Similar to DRAM Cache in KNL: Direct-mapped, Tags in ECC
Notes: However, a DRAM cache organization would need tags to differentiate the multiple lines that could map into it.
A way to add tags without needing multiple accesses is to store tags alongside each data (like in Alloy cache), and always read this TAG-AND-DATA together
This organization avoids the serialized request for tag then data. And, as requests can be serviced with just one DRAM access, such an organization achieves low hit-latency and efficient bandwidth usage.
We use this organization as our baseline, as the DRAM Cache in Knights Landing is similarly designed—with 72B Tag+Data+ECC.

## Slide 6: 3D-DRAM Cache Bandwidth is important
Chart: Speedup
| SPEC RATE | SPEC MIX | GAP | ALL26
2x Capacity | 1.103 | 1.0418 | 1.1401 | 1.1017
2x Bandwidth, 2x Capacity | 1.2343 | 1.2002 | 1.1925 | 1.2193
2x-capacity cache improves performance by 10%.
And, additional 2x bandwidth increases speedup to 22%.
Improving both bandwidth and capacity is valuable.
On 8-CPU, 1GB DRAM Cache configuration
10%
22%
Notes: DRAM caches already allow one to invisibly speed up memory accesses significantly (Intel Knights Landing and AMD High-Bandwidth Cache).
We want to see what the potential benefit is if we further improve the systems in terms of capacity and bandwidth, with, say, compression.
Y-axis is speedup.
X-axis is geomean of workloads. SPEC RATE is 8-core spec workloads, SPEC MIX refers to 8-core multi-programmed spec workloads, GAP refers to graph workloads, and ALL26 is the geomean of all workloads tested in our study.
We show a 2x-capacity DRAM cache (from 1 to 2GB)to see potential improvements from capacity.
And we show a 2x Capacity, 2x Channel system to see potential from doubling both capacity and bandwidth.
If we could improve capacity to 2x, we could achieve 10% speedup.
But if we could also improve bandwidth, we could achieve up to 22% speedup.
As such, we aim to use compression to improve not only capacity, but bandwidth as well, to achieve the higher 22% potential.

## Slide 7: INTRODUCTION: DRAM CACHE
Baseline: Direct-Mapped, One Data Block in an access
A
D
Baseline
C
B
A
B
C
D
7
A
Spatial
Indexing
(Incompressible)
C
Y
W
A
D
Traditional
Compression
(Incompressible)
C
B
A
D
Spatial Indexing
(Compressible)
C
B
W
X
Y
Z
Notes: As previously stated, practical DRAM caches are direct-mapped for hit-latency and bandwidth.
If we access lines A,B,C,D, they would map to set 0,1,2,3 in the DRAM cache.
If we want to read the lines, we would need 4 accesses.

## Slide 8: INTRODUCTION: COMPRESSED DRAM CACHE
Compression: Adds capacity, improve bandwidth?
A
B
C
D
A
D
Traditional
Compression
(Compressible)
C
B
W
X
Y
Z
A
Spatial
Indexing
(Incompressible)
C
Y
W
A
D
Traditional
Compression
(Incompressible)
C
B
A
D
Spatial Indexing
(Compressible)
C
B
W
X
Y
Z
1x
Bandwidth
Notes: If we could compress all lines to half the size. We could fit an additional line in every physical location. For example, we could additionally fit lines W, X, Y, and Z.
And, when we read A, we get both lines A and W. However, W is from a different context and is unlikely to be used shortly after so this type of compression is purely for capacity.

## Slide 9: INTRODUCTION: COMPRESSED DRAM CACHE
Compression: Adds capacity, improve bandwidth?
A
B
C
D
A
D
Traditional
Compression
(Incompressible)
C
B
A
D
Traditional
Compression
(Compressible)
C
B
W
X
Y
Z
A
Spatial
Indexing
(Incompressible)
C
Y
W
A
D
Spatial Indexing
(Compressible)
C
B
W
X
Y
Z
1x
Bandwidth
Notes: And, when lines are incompressible, we do no worse than the baseline as we could still fit our lines A,B,C, and D.
This is how cache compression has been proposed traditionally.

## Slide 10: INTRODUCTION: COMPRESSED DRAM CACHE
A
D
Traditional
Compression
(Compressible)
C
B
W
X
Y
Z
A
D
Traditional
Compression
(Incompressible)
C
B
Compression: Adds capacity, improve bandwidth?
A
B
C
D
4 accesses
@
1x-2x Capacity
A
Spatial
Indexing
(Incompressible)
C
Y
W
A
D
Spatial Indexing
(Compressible)
C
B
W
X
Y
Z
Notes: Thus, this type of cache compression achieves 1-2x capacity of an uncompressed cache.

## Slide 11: INTRODUCTION: COMPRESSED DRAM CACHE
Compression: Adds capacity, improve bandwidth?
A
B
C
D
A
D
Spatial Indexing
(Compressible)
C
B
W
X
Y
Z
2x
Bandwidth
A
D
Traditional
Compression
(Compressible)
C
B
W
X
Y
Z
A
D
Traditional
Compression
(Incompressible)
C
B
A
Spatial
Indexing
(Incompressible)
C
Y
W
Notes: So, how do we improve bandwidth?
We notice that the prior scheme read out two lines at once: A and W.
If both of the lines that were read out were useful if installed. In one access, you could get two useful lines. This would improve your effective bandwidth.
So, if you say compressed adjacent lines together, in a Spatial Indexing scheme. You could read A, and B, in one access; C and D, in another. You can read out your 4 lines in half the number of accesses, for 2x effective bandwidth. And also capacity.

## Slide 12: INTRODUCTION: COMPRESSED DRAM CACHE
Compression: Adds capacity, improve bandwidth?
A
B
C
D
A
Spatial
Indexing
(Incompressible)
C
Y
W
B,D?
< 1x
Bandwidth
A
D
Traditional
Compression
(Compressible)
C
B
W
X
Y
Z
A
D
Traditional
Compression
(Incompressible)
C
B
A
D
Spatial Indexing
(Compressible)
C
B
W
X
Y
Z
Notes: But, the problem is what happens when lines are incompressible.
If we tried to compress A and B together, but they do not fit in a physical location, only one of either A or B could be resident at a time.
This would mean half of your accesses (say for lines B and D) would need to go to memory, which would degrade your performance significantly.

## Slide 13: INTRODUCTION: COMPRESSED DRAM CACHE
Compression: Adds capacity, improve bandwidth?
Compressible
Incompressible
2x
Bandwidth
< 1x
Bandwidth
Incompressible
Compressible
Traditional Compression
Spatial Indexing
1x
Bandwidth
1x
Bandwidth
Notes: Thus we have our static indexing schemes.
One traditional compression sustains bandwidth under different compressibility.
And one spatial indexing scheme that improves bandwidth under compressible workloads, but degrades performance under incompressible workloads.

## Slide 14: INTRODUCTION: Traditional Compression
Chart: Speedup
| SPEC RATE | SPEC MIX | GAP | ALL26
Traditional Set Indexing | 1.0414 | 1.0283 | 1.2107 | 1.0761
2x Capacity | 1.103 | 1.0418 | 1.1401 | 1.1017
2x Bandwidth, 2x Capacity | 1.2343 | 1.2002 | 1.1925 | 1.2193
Compression for capacity (TSI) sees little speedup (7%)
due to diminishing returns on giga-scale caches
Improves Capacity
No degradation
Little speedup (7%)
Notes: Here is the performance of traditional cache compression for DRAM cache.
Blue is traditional set indexing compression. Purple, on the right is an organization with 2x-capacity 2x-bandwidth DRAM cache.
Some workloads benefit from the increased capacity. But many workloads see see diminishing returns on already-giga-scale caches.
However, we do note that is little slowdown. As such, this is a good baseline indexing scheme.
Compression for purely capacity achieves 7% speedup, short of the 10% we hoped to achieve from 2x capacity, as not all lines are compressible.
To achieve higher performance, we aim to additionally improve bandwidth

## Slide 15: INTRODUCTION: SPATIAL Indexing
Chart: Speedup
| SPEC RATE | SPEC MIX | GAP | ALL26
Spatial Indexing | 0.86412 | 0.98361 | 1.5012 | 1.0013
2x Capacity | 1.103 | 1.0418 | 1.1401 | 1.1017
2x Bandwidth, 2x Capacity | 1.2343 | 1.2002 | 1.1925 | 1.2193
Spatial Indexing compression gets both benefits of bandwidth and capacity when lines are compressible. But, it hurts performance when lines are incompressible
Improves Bandwidth
Can degrade
No speedup
Notes: Graph workloads see significantly improvement due to both bandwidth and capacity improvements.
However, many SPEC workloads have lines that do not have good compressibility ratio. As such, SPEC workloads see significant degradation in performance.
In total, this spatial indexing scheme provides no benefit on average.

## Slide 16: INTRODUCTION: COMPRESSED DRAM CACHE
Compressible
Incompressible
< 1x
Bandwidth
1x
Bandwidth
Goal: Compression for Capacity AND Bandwidth
Compressible
2x
Bandwidth
Incompressible
DICE (Dynamic Index)  19% Speedup + 36% EDP
Spatial Indexing
Traditional Compression
1x
Bandwidth
Notes: Our goal is to effectively switch between the two schemes to achieve
bandwidth benefits when lines are compressible, and
Sustain bandwidth when lines are incompressible.
Our dynamic scheme achieves 19% speedup (close to 22% possible from 2x bandwidth and capacity cache) and 36% reduction in energy-delay-product.

## Slide 17: DICE OVERVIEW
Compressed DRAM Cache Organization
Flexible Mapping for Quick Switching
Dynamic Indexing ComprEssion (DICE)
  Insertion Policy
  Index Prediction
Notes: First, we talk about how to design a compressed DRAM Cache Organization.

## Slide 18
L3 Cache
L4 Cache Controller
Memory
DRAM Cache
Writeback
Install
Read
Write
Compression Logic
Decompression Logic
DRAM Cache (compressed)
On-chip
Off-chip
Compression: Simple changes within the controller
PRACTICAL DRAM CACHE COMPRESSION
Notes: Here we have an L3 cache, main memory, and a DRAM Cache between them.
The off-chip DRAM Cache is accessed by an on-chip cache controller. All reads and writes to DRAM cache are managed by this cache controller.
We notice that we can implement cache compression simply by adding compression logic before every write, and decompression logic after every read. Thus, we can implement compression with changes local to the cache controller (does not need changes to HBM or bus protocols).
But how do we handle the tags in such a case.

## Slide 19: DRAM CACHE TAG format
Tag A
Data A
Tag Boundary
Data
Cache controller receives 72B of tag+data. It can flexibly interpret bits as tag bits or data bits.
8 Bytes
64 Bytes
Notes: We note that every access to the DRAM cache reads 72B from the DRAM Array.
Current organizations interpret 8-Bytes of it as Tag, and 64-Bytes of it as Data.
However, we note that it is up to the controller to determine them as either tag or data bits. We can actually have it flexibly interpret bits as tag or data bits as needed.

## Slide 20: PROPOSED FLEXIBLE TAG FORMAT
A
B
I
X
A
B
X
Is Tag?
Tag Boundary
Data
Not Tag
Is Tag?
Is Tag?
We create Tag space as needed, for up to 28 lines. Achieves 1.6x effective capacity.
Notes: As such, we can dynamically create allocate space for tags, by using data space. We can simply keep a bit per tag, telling us whether or not to interpret the next couple bytes as Tag, or Data.
This enables us to store as many as 14-28 lines in every physical location.
In practice, we see 1.6x effective capacity in our workloads.

## Slide 21: DICE OVERVIEW
Compressed DRAM Cache Organization
Flexible Mapping for Quick Switching
Dynamic Indexing ComprEssion (DICE)
  Insertion Policy
  Index Prediction
Notes: So now we have our Compressed DRAM Cache Organization.
Now, in our to implement our dynamic compression scheme, we need to be able to switch quickly between the two policies.

## Slide 22: Flexible Mapping (TSI or BAI)
5
7
0
1
2
3
4
5
6
7
0
4
2
6
1
3
Traditional Set Indexing (TSI)
Bandwidth-Aware Indexing (BAI)
4
6
5
7
0
2
1
3
Naïve Spatial Indexing
Bandwidth-Aware Indexing (BAI) facilitates quick switching between two indices TSI and BAI.
Notes: Traditional Set Indexing maps adjacent lines in adjacent sets.
Naïve spatial Indexing maps 2 adjacent lines to every 1.
However, it shifts nearly every line from its original position (only first and last entry in same location).
Instead, we choose to shift half of each pair of lines, to their neighbor. For example, stuff 0 and 1, into set 0. stuff 2 and 3, into set 2. We still get the bandwidth benefits of Spatial Indexing. But, in addition, only half of the lines are shifted from their original position.
Switching can be done efficiently as only half of lines need to move. And entries are guaranteed to be in the same row buffer.

## Slide 23: Flexible Mapping (TSI or BAI)
1
2
3
4
5
6
5
7
0
1
2
3
4
5
6
7
0
4
2
6
1
3
Traditional Set Indexing (TSI)
Bandwidth-Aware Indexing (BAI)
7
0
Naïve Spatial Indexing
Bandwidth-Aware Indexing (BAI) facilitates quick switching between two indices TSI and BAI.
Notes: Traditional Set Indexing maps adjacent lines in adjacent sets.
Naïve spatial Indexing maps 2 adjacent lines to every 1.
However, it shifts nearly every line from its original position (only first and last entry in same location).
Instead, we choose to shift half of each pair of lines, to their neighbor. For example, stuff 0 and 1, into set 0. stuff 2 and 3, into set 2. We still get the bandwidth benefits of Spatial Indexing. But, in addition, only half of the lines are shifted from their original position.
Switching can be done efficiently as only half of lines need to move. And entries are guaranteed to be in the same row buffer.

## Slide 24: Flexible Mapping (TSI or BAI)
5
7
0
1
2
3
4
5
6
7
0
4
2
6
1
3
Traditional Set Indexing (TSI)
Bandwidth-Aware Indexing (BAI)
4
6
5
7
0
2
1
3
Naïve Spatial Indexing
Bandwidth-Aware Indexing (BAI) facilitates quick switching between two indices TSI and BAI.
4
6
1
3
Notes: Traditional Set Indexing maps adjacent lines in adjacent sets.
Naïve spatial Indexing maps 2 adjacent lines to every 1.
However, it shifts nearly every line from its original position (only first and last entry in same location).
Instead, we choose to shift half of each pair of lines, to their neighbor. For example, stuff 0 and 1, into set 0. stuff 2 and 3, into set 2. We still get the bandwidth benefits of Spatial Indexing. But, in addition, only half of the lines are shifted from their original position.
Switching can be done efficiently as only half of lines need to move. And entries are guaranteed to be in the same row buffer.

## Slide 25: DICE OVERVIEW
Compressed DRAM Cache Organization
Flexible Mapping for Quick Switching
Dynamic Indexing ComprEssion (DICE)
  Insertion Policy
  Index Prediction
Notes: Next, we talk about our dynamic indexing scheme.

## Slide 26: DICE: Dynamic-indexed Compressed Cache
DRAM Cache
Compressibility Based Insertion
Install
Read
DICE: Dynamic-Indexing Cache comprEssion,
decides index on install, and predicts index on read
Cache Index Prediction
Bandwidth-Aware Index
Traditional Set Index
TSI = BAI
?
?
Notes: DICE: Dynamic-Indexed Compressed Cache Overview.
Decide index on install.
Predict index on read.
Because if you check both. You waste the bandwidth benefits offered by compressed cache organization.
We limit our scheme to only affect eviction and installs (and do not do explicit swaps, to save bandwidth and keep controller simple).

## Slide 27: Compressibility-based Insertion
DRAM Cache
Compressibility Based Insertion
Install
Compressibilty-based insertion uses Bandwidth-Aware Indexing when lines are compressible, and TSI otherwise
Bandwidth-Aware Index
Traditional Set Index
TSI = BAI
> ½-size
<= ½-size
?
But checking both wastes bandwidth
No explicit swaps. Eviction and install decides policy
Read
Notes: DICE Overview:
We want to use Bandwidth-Aware Indexing (our spatial indexing) when lines are compressible, and Traditional Set Indexing when lines are incompressible.
As such, we have a simple index decision policy.
If a line compresses to greater than half of a line size, assume it cannot compress with neighbor and insert in TSI. This way, it is likely to do no harm.
If a line compresses to less than half of a line size, assume neighbor also compresses to less than half so they can compress together.
With compressibility-based insertion, we can install opportunistically into bandwidth-aware index, to get both benefits of bandwidth and capacity.
And fallback to traditional set indexing when lines are incompressible.
Note that installs are done independently of neighbor to reduce dependency on adjacent lines and simplify cache organization.
But checking both indices wastes the bandwidth we worked so hard to get.
We do prediction to still get the line in one access.

## Slide 28: SIMILAR INTRA-Page COMPRESSIBILITY
Indices seen in a Compressible Page
Install
DICE is likely to install lines of a page into similar index
Bandwidth-Aware Index
Bandwidth-Aware Index
Bandwidth-Aware Index
<= ½-size
Read BAI
Lines within a page have similar compressibility
Notes: DICE Overview:
We want to use Bandwidth-Aware Indexing (our spatial indexing) when lines are compressible, and Traditional Set Indexing when lines are incompressible.
As such, we have a simple index decision policy.
If a line compresses to greater than half of a line size, assume it cannot compress with neighbor and insert in TSI. This way, it is likely to do no harm.
If a line compresses to less than half of a line size, assume neighbor also compresses to less than half so they can compress together.
With compressibility-based insertion, we can install opportunistically into bandwidth-aware index, to get both benefits of bandwidth and capacity.
And fallback to traditional set indexing when lines are incompressible.
Note that installs are done independently of neighbor to reduce dependency on adjacent lines and simplify cache organization.
But checking both indices wastes the bandwidth we worked so hard to get.
We do prediction to still get the line in one access.

## Slide 29: SIMILAR INTRA-Page COMPRESSIBILITY
Indices seen in an Incompressible Page
Install
Thus, page-based last-time prediction of index
can be accurate (94%)
Traditional Set Index
Traditional Set Index
Traditional Set Index
> ½-size
Read TSI
Traditional Set Index
Bandwidth-Aware Index
Lines within a page have similar compressibility
2nd access only on mispredict
Notes: DICE Overview:
We want to use Bandwidth-Aware Indexing (our spatial indexing) when lines are compressible, and Traditional Set Indexing when lines are incompressible.
As such, we have a simple index decision policy.
If a line compresses to greater than half of a line size, assume it cannot compress with neighbor and insert in TSI. This way, it is likely to do no harm.
If a line compresses to less than half of a line size, assume neighbor also compresses to less than half so they can compress together.
With compressibility-based insertion, we can install opportunistically into bandwidth-aware index, to get both benefits of bandwidth and capacity.
And fallback to traditional set indexing when lines are incompressible.
Note that installs are done independently of neighbor to reduce dependency on adjacent lines and simplify cache organization.
But checking both indices wastes the bandwidth we worked so hard to get.
We do prediction to still get the line in one access.

## Slide 30: PAGE-based Cache INDEX PREDICTOR (CIP)
Page-based last-time prediction exploits similar intra-page compressibility, to achieve high prediction accuracy (94%)
0
1
0
0
0
1
1
1
Page #
Hash
Demand Access
Predict Traditional Set Index
0 = Traditional Set Index
1 = Bandwidth-Aware Index
Last-Time Table (LTT)
Notes: Predict index on read.
If check both. You waste bandwidth benefits offered by compressed cache organization.
How do we predict?
We notice that lines within a page are likely to have similar compressibility. If we see a line from a page was previously installed in BAI, we assume the other lines in that page were also installed in BAI. As such, we can predict that future accesses to the page will likely find the line in the BAI index.
We implement this by having a last-time table that tracks a last index seen for a particular page. We hash this into a structure to save space. <1KB.

## Slide 31: DICE OVERVIEW
Compressed DRAM Cache Organization
Flexible Mapping for Quick Switching
Dynamic Indexing (DICE)
  Insertion Policy
  Index Prediction
Results

## Slide 32: Methodology (1/8th Knights Landing)
Core Chip
  3.2GHz 4-wide out-of-order core
  8 cores, 8MB shared last-level cache
Compression
  FPC + BDI
Stacked DRAM
Commodity DRAM
CPU
Notes: 8-cores (1/8th of 64 KNL core-count)
8MB shared last-level cache
Compression algorithms used in this study were Frequent Pattern Compression and Base-Delta Immediate Compression. Algorithm used is orthogonal to study as any can be substituted.

## Slide 33: Methodology (1/8th Knights Landing)
Stacked DRAM
Commodity DRAM
 | Stacked DRAM | Commodity DRAM
Capacity | 1GB | 32GB
Bus | DDR1.6GHz, 128-bit | DDR1.6GHz, 64-bit
Channels | 4 channels | 1 channel
Bandwidth | 100 GBps | 12.5 GBps
Latency | 35ns | 35ns
CPU
Other sensitivities in paper
Notes: 1GB stacked DRAM.
4 channels, with 128-bit bus-width. ~100 GBps (1/8th of KNL bandwidth)
Iso-latency with DRAM, given current HBM products.
32GB DIMM-based DRAM

## Slide 34: DICE RESULTS
Chart: Speedup
| SPEC RATE | SPEC MIX | GAP | ALL26
Traditional Set Indexing | 1.0414 | 1.0283 | 1.2107 | 1.0761
Spatial Indexing | 0.86412 | 0.98361 | 1.5012 | 1.0013
DICE | 1.1221 | 1.0746 | 1.4888 | 1.1898
DICE improves performance over both Spatial Indexing and Traditional Indexing with fine-grain decision (19%)
Performs as Spatial
Indexing
Performs as Traditional
Indexing
DICE outperforms both
Notes: DICE is able to use Bandwidth-Aware-Indexing when workload is compressible.
And Traditional-Set-Indexing, when workload is incompressible.
But, it often improves performance over both as it can aggressively use BAI for compressible portions of workloads, and fallback to TSI when lines are compressible. As such, workloads with mixed levels of compressibility see huge improvements under DICE.
DICE achieves 19% speedup, close to the ideal 2x capacity, 2x bandwidth DRAM cache.

## Slide 35: INTRODUCTION: COMPRESSED DRAM CACHE
Compressible
Incompressible
< 1x
Bandwidth
1x
Bandwidth
Goal: Compression for Capacity AND Bandwidth
Compressible
2x
Bandwidth
Incompressible
DICE (Dynamic Index)  19% Speedup + 36% EDP
Spatial Indexing
Traditional Compression
1x
Bandwidth
Notes: DICE: Dynamic-indexing compression achieves 2x bandwidth when workloads are compressible, and does not degrade performance when workloads are incompressible.
DICE improves performance by 19%, close to the 22% speedup offered by a 2x-capacity 2x-channel system.
Thank you

## Slide 36: Thank you

## Slide 37: Extra SLIDES
Extra Slides

## Slide 38: DIFFERENT CACHE SENSITIVITIES
Notes: Better latency accesses.
2x channels. More of a memory bandwidth bottleneck. Capacity benefits are more pronounced.

## Slide 39: Comparison to prefetch

## Slide 40: Comparison to sram /memory compression

## Slide 41: FULL RESULTS (mixed compressibility)

## Slide 42: SRAM Cache compression on DRAM CACHE

## Slide 43: Distribution for index decision

## Slide 44: DICE INSERTION threshold

## Slide 45: EFFECTIVE CAPACITY

## Slide 46: L3 hit rate improvement

## Slide 47: Larger TSI vs. BAI example